## Slide 1
digitalent.kominfo.go.id
DTS 2019
Internet of Things
28 IoT Device Management

## Slide 2: Topik Bahasan
Overview
Device management
Device management standards
LWM2M

## Slide 3: Security – Remote Firmware Update

## Slide 4: Security – Easy Bug Fixes Update

## Slide 5: Remote and Difficult to Access Location

## Slide 6: Constrained Devices and Networks

## Slide 7: Power Challenges

## Slide 8: Device Management
Configure the device
  Reboot
  Update APN, current date/time, …
Update the firmware / OTA update
Manage the software
  Change settings
  Access logs
Monitor and gather connectivity statistics

## Slide 9: Device Management Standards
TR-069 - Fixed network broadband DSL routers
OMA DM - Mobile phones
SNMP - Enterprise IP networks
OMA LWM2M - IoT constrained devices

## Slide 10: LWM2M
LightweightM2M is originally a Device Management technology
Extended to support generic data exchange

## Slide 12: LWM2M
Open Mobile Alliance (OMA) protocol
Designed for Machine to Machine or IoT device management
Communication between LwM2M Server to LwM2M client
Developed for sensor networks
Managing lightweight and low power constrained devices
Based on representational state transfer (REST)
Created for remote management of M2M devices
Enable various IoT services

## Slide 13: LWM2M
Secured data transfer – Constrained Application Protocol (CoAP)- IPSO
Based on working group standards from IETF (Internet Engineering task force)
Supported by Eclipse Foundation. Implemented:
  Leshan – Java
  Wakaama – C

## Slide 14: LWM2M Purpose
Provide Device Management functionality over sensor or cellular networks
Transfer service data from the network to devices
Extend to meet the requirements of most any application

## Slide 15: LWM2M Flow Diagram

## Slide 17: Protocol Layers and IoT Standards

## Slide 18: Role of LwM2M Devices in IoT
Designed to create the following opportunities and business benefits for the M2M industry:
Reduce the degree of fragmentation (perbedaan versi)
Enabling more plug-and-play solutions
Act as an enabler to grow the M2M market in various segments ranging from
  Smart city
  Energy management
  Location tracking.
  Low cost to enable sustainable business models.

## Slide 19: Role of LwM2M Devices in IoT
Improve time-to-market and the manageability of devices
Lead to a decoupling of M2M appliances and server-side platforms, thereby enabling independent innovation of M2M devices and platforms.
Growing the number of interoperable M2M connected devices to provide more choice for M2M customers regarding M2M devices and their management platforms.

## Slide 20: Advantages LWM2M Implementation
Reduce the cost
Save the time
Reduce risk
Unlocks the door for new innovations.

## Slide 21: Block Diagram

## Slide 22: LWM2M Security
In LWM2M, security is provided by:
Transport layer security (DTLS)
Access control on objects determined per LwM2M Server

## Slide 23: LWM2M Features
Firmware upgrade (in band or over HTTP)
Device monitoring and configuration
Server provisioning (bootstraping)

## Slide 24: LWM2M: standard objects
Device
Server
Connectivity monitoring
Connectivity statistics
Location
Firmware
LwM2M objects have a numerical identifier
(Device = 3, Location = 6, …)

## Slide 25: LWM2M URIs
URLs:
/{object}/{instance}/{resource}
Example:
/6/0 = whole position object (binary TLV)
/6/0/2 = only the altitude value

## Slide 26: Praktek
Wakaama
Create object
Configure
Active loop

## Slide 27: Wakaama
A C client and server implementation of LwM2M
Not a shared library (.so/.dll)
POSIX compliant and embedded friendly
Plug your own IP stack and DTLS implementation

## Slide 28: Features
Register, registration update, deregister
Read, write resources
Read, write, create, delete object instances
TLV or plain text
Observe

## Slide 29: Create Object
lwm2m_object_t * get_object_device()
{
lwm2m_object_t * deviceObj;
deviceObj = (lwm2m_object_t *)lwm2m_malloc(sizeof(lwm2m_object_t));
if (NULL != deviceObj)
{
memset(deviceObj, 0, sizeof(lwm2m_object_t));
deviceObj->objID = 3;
deviceObj->readFunc = prv_device_read;
deviceObj->writeFunc = prv_device_write;
deviceObj->executeFunc = prv_device_execute;
deviceObj->userData = lwm2m_malloc(sizeof(device_data_t));
if (NULL != deviceObj->userData)
{
((device_data_t*)deviceObj->userData)->time = 1367491215;
strcpy(((device_data_t*)deviceObj->userData)->time_offset, "+01:00");
}
else
{
lwm2m_free(deviceObj);
deviceObj = NULL;
}
}
return deviceObj;
}

## Slide 30: Configure
objArray[0] = get_object_device();
if (NULL == objArray[0])
{
fprintf(stderr, "Failed to create Device object\r\n");
return -1;
}
objArray[1] = get_object_firmware();
if (NULL == objArray[1])
{
fprintf(stderr, "Failed to create Firmware object\r\n");
return -1;
}
objArray[2] = get_test_object();
if (NULL == objArray[2])
{
fprintf(stderr, "Failed to create test object\r\n");
return -1;
}
lwm2mH = lwm2m_init(prv_connect_server, prv_buffer_send, &data);
if (NULL == lwm2mH)
{
fprintf(stderr, "lwm2m_init() failed\r\n");
return -1;
}
result = lwm2m_configure(lwm2mH, "testlwm2mclient", BINDING_U, NULL,
OBJ_COUNT, objArray);
...
result = lwm2m_start(lwm2mH);

## Slide 31: Active Loop
while (0 == g_quit)
{
struct timeval tv;
tv.tv_sec = 60;
tv.tv_usec = 0;
/*
* This function does two things:
* - first it does the work needed by liblwm2m (eg. (re)sending some packets).
* - Secondly it adjust the timeout value (default 60s) depending on the
* state of the transaction (eg. retransmission) and the
* time between the next operation
*/
result = lwm2m_step(lwm2mH, &tv);
if (result != 0)
{
fprintf(stderr, "lwm2m_step() failed: 0x%X\r\n", result);
return -1;
}
}

## Slide 32: Example
https://github.com/kartben/Wakaama-mbed

## Slide 33: Sesi Lab 1
Carilah kasus/problem terkait Firmware Update
  Kasusnya apa
  Dampaknya bagaimana
Waktu: 30 menit (kelompok maks 4 orang)
  Output: ppt
  Dipresentasikan

## Slide 34: Sesi Lab: Instalasi Leshan Server

## Slide 35
digitalent.kominfo
digitalent.kominfo
DTS_kominfo
Digital Talent Scholarship 2019
IKUTI KAMI
Pusat Pengembangan Profesi dan Sertifikasi
Badan Penelitian dan Pengembangan SDM
Kementerian Komunikasi dan Informatika
Jl. Medan Merdeka Barat No. 9
(Gd. Belakang Lt. 4 - 5)
Jakarta Pusat, 10110
digitalent.kominfo.go.id